## Slide 1
The slides used in this presentation are intended to be used in an event with verbal elaboration by a knowledgeable presenter. The slides highlight key U.S. product safety requirements for discussion. The text is not a comprehensive statement of legal requirements or policy and should not be relied upon for that purpose. Moreover, with the passage of time, it may not reflect the latest information. You should consult official versions of U.S. statutes and regulations, as well as published CPSC guidance when making decisions that could affect the safety and compliance of products entering U.S. commerce.

## Slide 2: Video: Welcome to the 2021 CPSC Podcast Series – Overview of Battery Safety Requirements

## Slide 3
Podcast Series 2021
Overview for Battery Safety Requirements
This presentation was prepared by CPSC Staff. It has not been reviewed or approved by the Commission and may not reflect its views.

## Slide 4: Biographies
Joseph Tsai, Senior Compliance Officer
Regulatory Enforcement Division
Office of Compliance and Field Operations
U.S. Consumer Product Safety Commission
Joseph joined the U.S. Consumer Product Safety Commission (CPSC) in April 2008, as a Compliance Officer in the Regulatory Enforcement Division of the Office of Compliance and Field Operations.
As a Compliance Officer, he is responsible for enforcing the mandatory regulations for children’s products, such as, toys, pacifiers, and rattles under the Federal Hazardous Substances Act (FHSA) and Consumer Product Safety Act (CPSA).
In addition, he advises stakeholders on requirements for tracking and certification for children’s products under the CPSA. His specific responsibilities include advisement on the implementation of regulations, standards, and bans under the FHSA and the CPSA, and providing advice and guidance to consumers and the regulated industry.
Prior to joining the CPSC, Mr. Tsai was an officer at U.S. Customs and Border Protection, and a research scientist with Scripps Research Institute, La Jolla, California. Mr. Tsai holds a Bachelor of Science degree from University of California, Los Angeles (UCLA), and a Master of Science degree from University of California, San Diego (UCSD).
Sylvia Chen
U.S. Consumer Product Safety Commission
Program Manager for East Asia and Pacific
Office of International Programs
Sylvia Chen is Program Manager for East Asia and Pacific at the U.S. Consumer Product Safety Commission (CPSC). In that role, she is responsible for managing the Commission’s bilateral and multi-lateral programs related to consumer product safety in Australia, Japan, Korea, Taiwan and New Zealand. She also supports the CPSC’s work with China. Since she joined the CPSC in 2008, Sylvia has been working with product safety regulators, industry organizations, manufacturers, exporters, buyers and other sourcing professionals to provide them with guidance and technical support in understanding U.S. requirements, in particular the latest requirements for consumer products. To that end, she has organized or coordinated many of the agency’s international education and outreach activities.
Sylvia has a Bachelor of Arts degree in English and American Literature from Peking University. In 1991, she graduated from The Ohio State University with a Master’s degree in East Asian

## Slide 5
$1 Trillion
Deaths, injuries, and property damage from consumer product incidents cost the nation more than $1 trillion annually.1
The US CPSC is a federal government agency charged with protecting the public from unreasonable risks of injury or death associated with the use of consumer products under the agency's jurisdiction.
CPSC is committed to protecting consumers from products that pose a fire, electrical, chemical, biological, or mechanical hazard.
CPSC's work to improve the safety of the more than 15,000 types of consumer products in its jurisdiction - such as toys, cribs, power tools, cigarette lighters, textiles, and household chemicals – has contributed to a decline in the rate of deaths and injuries associated with consumer products over the past 40 years.
1 https://www.cpsc.gov/s3fs-public/FY2019PBR.pdf

## Slide 6
CPSC’s Podcast Series 2021
Podcast | Topics
#1 | Overview of Children’s Sleepwear Requirements
#2 | Enhancing the Safety of Emerging Technology through Risk Assessment: Wearables
#3 | Overview of Battery Safety Requirements
#4 | Overview of Gates and Enclosures Requirements
#5 | Overview of Consumer Safety and Micromobility Devices
#6 | Overview of Cribs and Play Yards Requirements
“Questions on this Presentation? Send an email to CPSCinChina@cpsc.gov”

## Slide 7: Overview of Battery Safety Requirements: Lithium-Ion Battery Safety for Consumer Products into the United States

## Slide 8: Overview
Electrical Product Safety
  Fire and Shock Data
Hazard Mitigation Strategies
  Industry Consensus Standards
  Technical Regulations
  15(j) Requirement
  Complying with Industry Consensus Standards
  CPSC Data Systems
  High-Energy Density Batteries Project
  Battery Recalls
    Root Causes
Case Study – Products with No Standard
Case Study – Products with Well-Established Standards
Best Manufacturing Practices - Assuring Safety of Lithium-Ion Cell-Powered Products

## Slide 9: Electrical Product Safety
Electricity is a powerful, useful energy source that is potentially hazardous.
Electrical product failures or misuse can cause hazards, such as:
  Fires
  Electric shock
  Thermal burns (from exposure to hot surfaces)
  Chemical burns (from batteries),
  Injuries (lacerations from moving parts) or
  Loss of critical function (a smoke alarm not signaling a fire).
Products that generate, distribute, or use electrical energy should be compliant with applicable standards and installed according to applicable electrical codes to help minimize safety risks to consumers from these products.

## Slide 10: Electrical Fire Data
67,900 structure fires
from electrical equipment per year
  660 deaths, 3,410 injuries $1.738 billion in property losses per year
Top electrical
Cooking equipment, such as range/ovens, microwaves and small appliances
Distribution systems, such as installed wiring
Heating and cooling equipment
1 Average base on 2015-2017 data

## Slide 11: Electric Shock Data
60 consumer product-related electrocutions per year
  Top four involved products:
  Large Appliances
  Small Appliances
  Power Tools
  Lighting Equipment
Electrocutions have declined over time with increases in products incorporating double insulation, battery power, and the implementation of ground-fault circuit interrupters.
1 Average based on 2004 - 2013 data

## Slide 12: Hazard Mitigation Strategies
CPSC staff uses a multipronged approach
Support improvements to industry consensus standards/codes
Distribute safety information to consumers
Create and enforce technical regulations and bans
Recall products with defects after identifying hazards through investigations

## Slide 13: Hazard Mitigation Strategies: Industry Consensus Standards
Staff relies on industry consensus standards to establish minimum levels of safety.
Most electrical product safety standards have been developed and maintained under the auspices of Underwriters Laboratories (UL). Other standards developers for electrical product safety include the Institute of Electrical and Electronics Engineers (IEEE) and the National Electrical Manufacturers Association (NEMA)

## Slide 14: Hazard Mitigation Strategies: Technical Regulations
Check the CPSC website or contact CPSC staff to determine what requirements your product needs to meet: https://www.cpsc.gov/Business--Manufacturing
Battery-operated toys, electric toys, and citizens band (CB) station antennas are some electrical products subject to technical regulations
CPSC statutes specify a consumer product safety technical regulation shall not be issued unless:
a current industry consensus standard is not likely to adequately reduce the risk of injury
there is not likely to be substantial compliance with the consensus standard
OR

## Slide 15: Hazard Mitigation Strategies: Technical Regulations for Electrical Products
Battery-Operated Toys
ASTM F963-17, The Standard Consumer Safety Specification for Toy Safety, which is a comprehensive standard addressing numerous hazards that have been identified with toys. CPSC incorporated this industry consensus standard into a mandatory standard for toys (16 CFR part 1250).
Electric Toys
16 CFR 1505 – Requirements for electrically operated toys or other electrically operated articles intended for use by children. This covers any toy, game, or other article designed, labeled, advertised, or otherwise intended for use by children that is intended to be powered by electrical current from nominal 120 volt branch circuits
CB Antennas
16 CFR part 1204 - Safety Standard for Omnidirectional Citizens Band Base Station Antennas

## Slide 16: Hazard Mitigation Strategies: The 15(j) Requirement
CPSC can recall products, or prevent importation of products, if they fail to meet critical safety requirements of a certain specific industry consensus standard
Section 15(j) of the CPSA provides authority to specify for any consumer product or class of consumer products, characteristics whose existence or absence are deemed a substantial product hazard under section 15(a)(2) of the CPSA.
A product within the scope of section 15(j) must have specific observable product characteristics that are required by a industry consensus standard.

## Slide 17: Hazard Mitigation Strategies: The 15(j) Requirement
The Commission has determined that products that do not comply with a 15(j) regulated requirement present a defect and are a substantial product hazard.
Therefore products that do not comply with an applicable 15(j) requirement cannot be imported into or sold within the US.
Handheld hair dryers, holiday lights, and extension cords are electrical products subject to 15(j) regulated requirements

## Slide 18: Hazard Mitigation Strategies: 15(j) Requirement - Handheld Hair Dryers
16 CFR § 1120.3(a) – Household and commercial handheld hair dryers must have an integral immersion protection circuit interrupter plug (as per UL 859 and UL 1727)

## Slide 19: Hazard Mitigation Strategies: 15(j) Requirement – Seasonal and Decorative Lighting Products
16 CFR § 1120.3(c) – Seasonal and decorative lighting products must meet the minimum wire size requirements of UL 588, have sufficient strain relief and include integral overcurrent protection.

## Slide 20: Hazard Mitigation Strategies: 15(j) Requirement – Seasonal and Decorative Lighting Products
Not In Scope
Class 2-powered Products
Solar-powered Products
Rope Lights/Luminaires

## Slide 21: Hazard Mitigation Strategies: 15(j) Requirement – Extension Cords
16 CFR § 1120.3(d) – Extension Cords must meet the minimum wire size requirements of UL 817, have sufficient strain relief, be properly polarized and indoor-use cords must have outlet covers while outdoor-use cords must be jacketed.

## Slide 22: Hazard Mitigation Strategies: 15(j) Requirement – Extension Cords
Not In Scope
Detachable Power Supply Cords
Relocatable Power Taps
Appliance Cords

## Slide 23: Hazard Mitigation Strategies: Complying with Industry Consensus Standards
Electrical products not subject to a regulation do not require certification by an accredited third party lab (e.g., UL, Intertek or CSA) to a industry consensus standard, but staff observes a high rate of voluntary compliance.
  Many retailers will only sell electrical products if they have been third party certified.
  Some states and municipalities require certification for all electrical products to be sold in those jurisdictions.
  The Occupational Safety and Health Administration (OSHA) requires certification by a Nationally Recognized Testing Laboratory (NRTL) for electrical products used in a workplace.
  CPSC staff strongly recommends that manufacturers or exporters/importers seek third party certification for their electrical products as a means of hazard mitigation.

## Slide 24: Hazard Mitigation Strategies: Complying with Standards
Compliance with applicable regulations, standards, and the NEC are highly effective ways to mitigate hazards from equipment that generates, distributes, or uses electrical energy.
CPSC statutes assign the responsibility for safe products to all parts of the supply chain.
Importers, although reliant on foreign producers, are responsible for the safety of products they bring into the United States
All responsible
Manufacturers
Importers
Distributors
Retailers

## Slide 25: Hazard Mitigation Strategies: Responsibility to Comply
Manufacturers and importers should follow best practices to ensure that their electrical products do not pose unreasonable risks of injury.
  Comply with consensus standards and technical regulations
  Obtain certification from an accredited lab to assure and demonstrate products meet applicable industry consensus standard
  Maintain quality and configuration control
    Assess impact of material or component substitutions

## Slide 26: Industry Consensus Standards Process: CPSC Staff Participation
Review standards for inadequacies
Analyze injury/death data for hazard patterns
Propose standards development or revisions
Conduct tests and evaluations to support findings
Participate in committees
This is an ongoing process that begins with staff gathering incident information from CPSC’s data collection systems.
With such a heavy reliance on industry consensus standards, staff is engaged in the process of maintaining adequacy of industry consensus safety standards, including addressing emerging hazards, by actively participating through development and proposal of new or modified requirements.

## Slide 27: Industry Consensus Standards Process: CPSC Data
Injury and potential injury incident data
Death certificates
In-depth investigations
National Electronic Injury Surveillance System
National Fire Incident Reporting System*
IPII
DTHS
INDP
NEISS
NFIRS
*NFIRS is operated by the United States Fire Administration

## Slide 28: CPSC Data: IPPI
CPSC Data
Saferproducts.gov is CPSC’s public portal for incident reports and searches
Medical Examiners and Coroners Alert Program (MECAP)
News Clips
Hotline Calls
Internet Reports
Compliance Reports
Federal and State Agency Referrals
Other Reports
  Provides anecdotal account of product-related incidents

## Slide 29: CPSC Data: DTHS
Contracts with 50 states
Purchase approximately 8,000 per year
Time lag
Daily review
Analytical use
  Death certificates provide specific details on death-related incidents caused by products but minimal product details

## Slide 30: CPSC Data: INDP
CPSC Field staff conduct follow-up investigations on selected initial incident reports
On-site Investigations
  Local-level collaboration
    Medical examiner
    Police
    Fire
  Sample collection opportunity
Telephone Interviews
INDP reports provide specific details on a product and its involvement in an incident

## Slide 31: CPSC Data: NEISS
National sample
  Data collected from approximately 100 hospital emergency rooms around the country
  Submitted daily by hospital coders
  Data weighted to provide consumer injury estimates nationwide
  About 395,000 consumer product-related injury reports annually
Data available from 1980 to present
Provides statistically significant data with details on product-related injuries, but less detail on specific products

## Slide 32: CPSC Data: NEISS Hospital Locations
San Juan

## Slide 33: CPSC Data: NEISS Variables
Treatment date
Case number
Age
Sex
Injury diagnosis (2)
Body part injured
Disposition from ED
Products involved (2)
Locale
Type/work-related
Fire dept. involvement
Intent
Race/ethnicity
Narrative (2 lines)

## Slide 34: CPSC Data: NEISS – Data Accessible at CPSC.gov

## Slide 35: CPSC Data: NFIRS
NFIRS is a collection of voluntarily reported fire incidents input by the attending fire service.
This is not a statistical sample, but staff uses these data in conjunction with the National Fire Protection Association’s annual national fire survey to develop annual estimates of fires and their causes.
https://www.cpsc.gov/s3fs-public/2015to2017ResidentialFireLossEstimates.pdf?lrPHs2JTqq5ijz9zvLHL3zfukzWUKw_X

## Slide 36: CPSC Hazard Mitigation Strategies: High-Energy Density Batteries Project
Since 2016, staff has been engaged in a project to address hazards associated with high energy density batteries in consumer products.
Efforts included industry consensus standards work, import surveillance and compliance, and industry, interagency, and intergovernmental cooperation. Staff issued two status reports on the project:
Status Report on High-Energy Density Batteries Project February 12, 2018 - https://www.cpsc.gov/s3fs-public/High_Energy_Density_Batteries_Status_Report_2_12_18.pdf?UksG80UJqGY0q4pfVBkbCuUQ5sNHqtwO
FY 2020 Status Report and Action Plan for the High-Energy Density Batteries Project March 2020 - https://www.cpsc.gov/s3fs-public/High%20Energy%20Density%20Batteries_Status%20Memo_FY20_1-6bCleared-04012020.pdf?Qj4t_otWKfBZYLpvu4l6sUvx9ZJfFc4f

## Slide 37: CPSC Hazard Mitigation Strategies: High-Energy Density Batteries Project
Also staff sponsored the Naval Surface Warfare Center Carderock Division to conduct a study on lithium battery technology and an evaluation of mitigation techniques for multi-cell battery pack failures, issuing the following reports:
Emerging Energy Storage Technologies October 2020 - https://www.cpsc.gov/s3fs-public/NSWCCD-63-TR-2020-39_Emerging-Energy-Storage-Technologies_DIS_A_VERSION_ForPostingVersion12012020.pdf?wYqrWGArQLL53BlqSYr8RfCwb2eiznIT
Evaluation of Cell-to-Cell Propagation in Lithium-Ion Batteries Containing 18650 Sized Cells January 2020 - https://www.cpsc.gov/s3fs-public/Consumer%20Product%20Safety%20Commission%20%28CPSC%29%20Staff’s%20Statement%20on%20Naval%20Surface%20Warfare%20Center%2C%20Carderock%20Division’s%20%28NSWCCD%29%20Report%20on%20“Evaluation%20of%20Cell-to-Cell%20Propagation%20in%20Lithium-Ion%20Batteries%20Containing%2018650%20Sized%20Cells”.pdf?KKybsoSCNBqeX46SxJbUq2NqkkzZk_Wd
Staff is continuing to evaluate means of mitigating multicell battery pack failures and is participating in a cooperative effort with Canadian and Mexican governments to evaluate power banks.

## Slide 38: Battery Product Recalls: Fiscal Years 2017-2020
From FY 2017 to FY 2020, there were 32 recalls of 15 different types of products, totaling nearly 1.75 M units
Product Type | Number of Recalls | TOTAL Units Recalled
Laptop/Notebook Computers | 8 | 880,132
Hoverboard/Self-balancing Scooter | 6 | 5,220
Power Bank | 4 | 448,243
Speakers | 2 | 205,621
Hand/Foot Warmers | 2 | 16,707
Guitar | 1 | 81,491
Motorized Blinds | 1 | 57,361
video Monitor | 1 | 26,423
Cellphone | 1 | 10,065
Lantern | 1 | 5,855
Sound Machine | 1 | 4,976
Skateboard | 1 | 3,490
Power Recliner | 1 | 2,185
Golf Cart | 1 | 1,049
Vape Pen | 1 | 384

## Slide 39: Battery Recalls: Top Four Recalls by Number of Units (2017-2020)
Firm | Product/Recall Number | No. of Units
Apple Inc. | Laptop 19-152 | 432,000
Amazon.com LLC | AmazonBasics Portable Power Bank 18-728 | 257,760
Daniel M. Friedman & Associates (Steven Madden Ltd) | Universal rechargeable power banks 19-017 | 170,500
Brookstone Stores, Inc. | Indoor/outdoor wireless speaker 19-090 | 164,511

## Slide 40: Battery Recalls: Recalls of Lithium-ion Battery Products – Root Causes
Quality-Control Problems in Cell Manufacturing
Improper placement of leads
Contaminants in cell
Uneven forming of cell
Poor quality welds
Insufficient electrode overlap
Physical damage to cell
Missing insulating tape on terminal tab
Battery Pack Design Problems
No safety circuits
Inadequate (or any) overcharge/over-discharge protection
Inadequate physical protection

## Slide 41: Battery Recalls: Recalls of Lithium-ion Battery Products – Example Root Cause
Cylindrical Cell Contamination – Certified Cell
Laptop overheating incidents revealed defective cells
Examined cells found to have metallic particles (iron) adhered to electrode
Metallic particles can perforate separator and short electrodes
Cell can overheat, possibly go into thermal runaway

## Slide 42: Battery Recalls: Recalls of Lithium-ion Battery Products – Example Root Cause
Cylindrical Cell Contamination – Certified Cell
Root Cause: Manufacturing error when electrode-cutting chuck was repositioned improperly - interference occurred, creating iron particles
Corrective Actions Taken by Manufacturer:
Corrected alignment of chuck by next shift
Tracked assembly line production from affected dates
Limited scope of recalled products
Implemented process to control further issues with chuck alignment
Reviewed and reduced other metal-to-metal processes in cell manufacturing

## Slide 43: Battery Recalls: General Cell Contamination Mitigation Actions
Processes used to mitigate cell contamination
  Magnets to capture loose ferrous particles
  Suction to capture other particles
  Air ventilation and filtration systems in production areas to minimize contaminants
  Cell dissection to look for foreign particles
  X-rays – non-destructive inspection for foreign particles and assembly anomalies
  CT Scanner – more detailed non-destructive inspection

## Slide 44: Battery Recalls: Root Cause – Physical Damage Example
Damaged outer foil in polymer cell
Can cause internal soft shorts
Mitigation Strategies
Improve handling procedures and enhance worker training
Conduct visual inspection before batteries leave the factory

## Slide 45: Battery Recalls: Root Cause – Electrode Overlap Example
* IEEE 1625 (Laptops) and IEEE 1725 (Cell phones) standards
Insufficient electrode overlap
May result in lithium plating at edges and eventual short circuit
Negative-to-positive electrode overlap > 100 µm*

## Slide 46: Battery Recalls: X-ray Analysis
X-rays and Computed Tomography x-rays are useful tools for cell screening, as well as failure analysis

## Slide 47: Battery Recalls: Analysis – Dissection and Visual Inspection
Each Layer thickness
Separator = 10 ~ 20 µm
Tabs = 20 ~ 80 µm
Cu and Al foil = 10 ~ 20 µm
Coatings = 40 ~ 60 µm
Excessive amplitude on ultrasonic welds can produce high peaks that could penetrate separator and cause shorts.

## Slide 48: Case Study: Products with No Existing Standard
In late 2015, hoverboards flooded the U.S. market
These units were powered by a rechargeable lithium-ion multicell battery pack; there was no existing industry consensus standard for the end product

## Slide 49: Case Study: Products with No Existing Standard
Almost immediately, incidents were occurring – fires and falls

## Slide 50: Case Study: Hoverboard Incident Data – November 2015 - May 2017
Over 165 fire incidents, causing over $3M in property damages
  Incidents occurred in 38 states
  During and after charging
  During and after riding
3 Deaths –1 fire (2 victims, young girls), 1 fall
Estimated over 10,000 Emergency Room Visits
  ~90% from falls, e.g. sudden stops and starts
  ~15% head injuries
  ~50% arm injuries
  ~40% fractures
  ~30% sprain/abrasions

## Slide 51: 2015/2016 CPSC Staff Assessments of Hoverboards
Staff examined incident units and tested exemplar units on a dynamometer and with riders
Fire incident units exhibited signs of thermal runaway leading to catastrophic failure of the entire battery pack
Units were largely similar in construction with 20 Type 18650 cylindrical lithium-ion cells in a 10S-2P (ten pairs of parallel-connected cells in series) configuration.

## Slide 52: Case Study: 2015/2016 CPSC Staff Assessments of Hoverboards
Battery management system (BMS) circuits did not incorporate thermal sensing to prevent cell charge/discharge outside of temperature specifications
Internal wiring not installed in accordance with standard practices to protect against damage/shorting:
  Loose wires not bundled/secure
  Wires routed through openings in cast metal that was not deburred
  Wiring not sheathed where passing through pivot

## Slide 53: 2015/2016 CPSC Staff Assessments of Hoverboards
Rider tests revealed peak battery currents over 20 A
Dynamometer tests showed battery case temperatures well above typical operating temperatures

## Slide 54: 2015/2016 CPSC Staff Assessments of Hoverboards - Conclusions
Inadequate BMS – Failed protective circuit safety analysis
Inadequate cells (pack) for system load requirements
Cells not certified to UL 1642 to ensure they have been manufactured in accordance with standards
Battery chargers not certified to standard (UL 1310, UL 1012, or UL 60950-1)
Wiring improperly secured and protected in the pivot base, exposed connections could cause short circuit
Units posed a risk of fire – over 500,000 units recalled

## Slide 55: Case Study: Products with Well-Established Standards
Even products designed and constructed under well-established standards and with high rates of third party certification can pose risks of fire when best practices are not closely followed.
Photo Source: Google images

## Slide 56: Case Study: Products with Well-Established Standards – Cell Phone Recalls
Despite adherence to industry consensus standards and products being certified, manufacturing errors occurred from two different cell manufacturers.
* Source: https://news.samsung.com/global/samsung-electronics-announces-cause-of-galaxy-note7-incidents-in-press-conference

## Slide 57: Case Study: Products with Well-Established Standards – Cell Phone Recalls
* Source: https://news.samsung.com/global/samsung-electronics-announces-cause-of-galaxy-note7-incidents-in-press-conference

## Slide 58: Case Study: Products with Well-Established Standards – Cell Phone Recalls
Consequently, the cell phone manufacturer reviewed its internal procedures to tighten its manufacturing controls to assure that it could detect problems. These included:
X-ray inspection of all cells to check battery corners
Voltage decay measurement procedures to identify cells with potential problems.
Increased sampling, cycling, dissection and examination of cycled cells.
Additional flexing tests of the phones
Proposed a review and upgrade of IEEE 1725

## Slide 59: Best Manufacturing Practices: Assuring Safety of Lithium-Ion Cell-Powered Products
Lithium Battery Safety Basics
There are various electrode chemistries including LCO, LMO, NMC, and LFP, which have different performance specs and varying levels of safety – be aware of the differences and make sure it’s the best one for the application
Cells contain flammable electrolytes - defective or abused cells can enter thermal runaway condition, producing extreme heat and energetic disassembly
Critical safety circuits to control voltage, current and temperature during charge and discharge keep cells within their safe operating area

## Slide 60: Best Manufacturing Practices – Assuring Lithium Cell Safety
*Japan Electronics and Information Technology Industries Association and Battery Association of Japan Source: http://home.jeita.or.jp/page_file/20110517171451_cub9MvYFEh.pdf
Maintain cells within their specified safety region during charging and discharging

## Slide 61: Best Manufacturing Practices – Assuring Lithium Cell Safety Addition Industry Guidance
Disable charging:
  If cell surface temperatures are exceeded
  If cell is below 3 V
    or initiate pre-charge charging rate
  When charge current drops to .05C (no trickle charging)
Balance cells in multi-cell packs
Assure that the charger is compatible with the cells/battery
*Source: http://batteryuniversity.com/learn/article/charging_lithium_ion_batteries

## Slide 62: Best Manufacturing Practices – Assuring Lithium Cell Safety Additional Guidance – Thermal Management
Use thermal sensors to monitor cell surface temperatures (red circles) and/or thermal insulators (green arrows) to avoid excess temperatures

## Slide 63: Best Manufacturing Practices – Assuring Lithium Cell Safety Select cells with Integral Protection
Current Interrupt Device (CID)
  Disconnects cell from terminal under excessive internal pressure
Resettable Positive Temperature Coefficient (PTC)
  Limits current (May not be suitable for high-drain applications)
  Does not protect against thermal runaway due to internal faults

## Slide 64: Best Manufacturing Practices – Assuring Lithium Cell Safety Select cells with Integral Protection
  User replaceable cells need an integral BMS to provided charge control and to protect against
  Over-charge
  Over-discharge
  External short-circuit
Source: https://batterybro.com/blogs/18650-wholesale-battery-reviews/18306003-battery-safety-101-anatomy-ptc-vs-pcb-vs-cid

## Slide 65: Best Manufacturing Practices – Assuring Lithium Cell Safety Staff Recommendations
Lithium-ion battery safety requires diligence from producer to user.
Lithium-ion battery products should:
  Be designed and built in accordance with applicable industry consensus standards; the system from charger to cell should be evaluated together for complete compatibility.
  Use high quality cells, suitable for the application
      In accordance with manufacturer’s specifications
  Be manufactured in strict accordance with industry standard quality control processes
      Maintain configuration control with only approved material or component substitutions subject to impact assessments

## Slide 66: Best Manufacturing Practices – Assuring Lithium Cell Safety Staff Recommendations
Staff recommends lithium-ion battery products:
  Be properly marked with warning labels to inform/educate users of the potential hazards and to closely follow manufacturer’s instructions for proper use
  Be third-party certified by an accredited laboratory
Under CPSC’s statutes, manufacturers, importers, distributors, and retailers are responsible to assure consumer products to do not present an unreasonable risk of injury or death.

## Slide 67: Questions?
Submit questions in English or Chinese to this podcast:
CPSCinChina@CPSC.GOV

## Slide 68
Resources

## Slide 69
Chinese Resources at cpsc.gov
https://www.cpsc.gov/zh-CN/Business--Manufacturing/Business-Education

## Slide 70
Chinese Resources at cpsc.gov
https://www.cpsc.gov/s3fs-public/HandbookforManufacturingChinese.pdf (中文版本 )
https://www.cpsc.gov/s3fs-public/pdfs/blk_pdf_handbookenglishaug05.pdf (英文版本)
https://www.cpsc.gov/s3fs-public/THE%20REGULATED%20PRODUCT%20HANDBOOK_050613%20CHN%20Final_0.pdf (中文版本 )
https://www.cpsc.gov/s3fs-public/RegulatedProductsHandbook.pdf (英文版本)

## Slide 71
CFR: Commercial Practices
https://www.govinfo.gov/content/pkg/CFR-2017-title16-vol2/pdf/CFR-2017-title16-vol2.pdf (英文版本)
CPSC Laboratory Manuals:
https://www.cpsc.gov/s3fs-public/Laboratory-test-manual-16-CFR-Part-1610-Ch.pdf?MhtbUWNy6jmOPx9b6f.RErt.n.2n_d_h (中文版本)
https://www.cpsc.gov/s3fs-public/Flammability%20of%20Clothing%20Textiles%20Test%20Manual_1610.pdf (英文版本)
Chinese Resources at cpsc.gov

## Slide 72
CPSC Business Resources
CPSC-Accepted Laboratories Search Page:
www.cpsc.gov/LabSearch
Definition of children’s product – 16 CFR Part 1200
Certificates of conformity – 16 CFR Part 1110
Third-party testing – 16 CFR Parts 1107, 1109, and 1112
Tracking information – 15 USC § 2063(a)(5)
Mandatory reporting requirements – 15 USC §2064

## Slide 73
http://business.cpsc.gov
Online tool designed specifically to help businesses comply with federal consumer product safety requirements.
Asks a series of guided questions, and based on the answers produces a downloadable (PDF) report.
Provides customized guidance with links to product safety regulations that may apply to the product and important information on labeling, certification and testing requirements.

## Slide 74: Regulatory Robot
Regulatory Robot is a tool to help identify which requirements are applicable
  Does not list details of requirements
User inputs product features
Regulatory Robot outputs list of requirements
User references source documents for specific requirements

## Slide 75
Battery Resources
For more information, please visit:
www.CPSC.gov
https://www.cpsc.gov/Regulations-Laws--Standards/Voluntary-Standards/Topics/Batteries/